Boat Inspection Checklist

On ramp inspection (before launching for test run):  (Check off, if okay.  Make notes if not okay)

| verify features from Feature List | current registration: boat & trailer | hull condition (scrapes, etc) |
| --- | --- | --- |
| stress cracks | chips/repairs evident | hand rails/cleats tight? |
| check horn | nav/anchor lights work | check ALL compartment lids |
| check bilge for fuel odors | look in bilge for water/oil/dirt/fuel | remove/reinstall bilge plug |
| are batteries safely mounted? | are battery terminals clean? | any loose/disconnected wires? |
| Is engine held by transom saver? | wiggle engine...mounted firmly? | any transom cracks? |
| inspect trailer tire wear pattern | check trailer tires for grease | check all trailer lights |

On the water inspection:  (check mark if okay.  make notes if not okay)

| engine started on _____ tries? | cold idle quality______________ | hot idle quality_______________ |
| --- | --- | --- |
| steering tight, loose, too tight? | check all gauges | check kill switch |
| check out trolling motor | test depth finders/electronics | check all pumps (fill livewell) |
| test ease of shifting: fwd & rev | how easy does it get on plane? | note water pressure at diff rpm’s |
| note RPM at WOT____________ | porpoising (midrange & WOT)? | chine walk? |
| acceleration (smooth at all rpm’s) | note steering torque: excessive? | test hydraulic jack plate (if avail.) |
| excessive smoke? | abnormal noise/vibration? | feel for water leaks under dash |

Back on the ramp inspection:  (check mark if okay.  make notes if not okay)

| does boat center on trailer okay? | does winch work properly? | check full livewell for leaking |
| --- | --- | --- |
| check bilge for fuel leaks/fumes check splashwell for fuel/oil leaks | check bilge for water | check under engine cowling for fuel or water leaks |

Test bilge pumps by removing the bilge plug with the boat secured back on the trailer with tie downs.   Back the boat/trailer into the water just far enough for water to enter the bilge with bilge pump(s) “on”. Wait while the bilge fills to see if the automatic bilge pump activates.

Notes for dealer review:__________________________________________________________________

_____________________________________________________________________________________

_____________________________________________________________________________________

_____________________________________________________________________________________

_____________________________________________________________________________________

If everything above checks out good, then it is time for a professional boat inspection and appraisal.